Design of a flash flood forecast model for the Shullcas River subbasin, Peru

B. Segura*, P. Lagos* and K. Takahashi**

*Instituto Geofísico del Perú

**University of Washington

( Abstract: The objective of the present work is to develop a statistical model to estimate variations in daily discharge in the Shullcas River subbasin (Huancayo-Peru), using satellite estimations of precipitation (Hydro-estimator Technique and the Convective Stratiform Technique) that could be used in real time, with hourly satellite rain estimates, to make short term flash flood predictions and provide warnings. Here we present some initial results on the validation of the precipitation estimates in the Shullcas River subbasin. We first validate the satellite estimations. The work compares the estimated discharge with measured discharge and rainfall to determine the technique that best reflects hydrologic and meteorologic data.

1 Introduction

The rains in the Central Andes of Peru according to the Climatic Atlas (IGP 2005), are well defined by a rainy period from January to March and dry from June to August. A study made by Segura (2006) using the technical Hydro-estimator (Vicente et al., 1998) for Mantaro river basin, has shown that the significant rainfall begin in October, is increased until arriving at his maximum value in February, soon the March and April diminish (Figure 1), that agrees with the Climatic Atlas (Figure 2). According to this study three zones of greater precipitation estimated by satellite have been identified, in the northwestern part, southwestern and southeastern and of smaller precipitation in the zone of the valley (Figure 3), this agrees with the Climatic Atlas (Figure 4).

Figure 1: Monthly average of the rainfall from satellite (Segura 2006)

Figure 2: Monthly climatology of the rainfall from Climatic Atlas (IGP 2005)

Figure 3: Annual average of the rainfall from satellite (Segura 2006)

Figure 4: Multiannual average of rainfall from Climatic Atlas (IGP 2005)

In the study made by Fashé (2005), the monthly rainfall estimated from satellite images GOES-8 on Peru during the summer season, were compared with the estimated by the TRMM. The correlation between the estimated rainfalls using technique CST/TMI and the TRMM was 0.87 in the Peruvian Andes, for February of the 2002, with a mean deviation of +48.8% with respect to the average measurement by the TRMM. The monthly rainfall rate from satellite is show in the Figure 5.

Figure 5: Monthly rainfall rate from satellite for February of the 2002 (Fashé 2005)

## 2 Technique description

CST/TMI: This technique calculates digital values of minimum temperature in infrared images. This algorithm determines if these values have convective or stratifom characteristic and respectively assigns an amount of big or small rain in an area (Adler et al. 1988, Negri et al. 2002).

Hydro-estimator: The technique of rain estimation by satellite was developed by Gilberto Vicente (1998) to produce automatically rain estimations for the U.S.A. It was developed in the National Oceanic and Atmospheric Administration/ National Environmental Satellite Data and Information Service (NOAA/NESDIS) and uses the infrared band (10.7(m) of the GOES satellite of space resolution 4x4 Km. The calculation is based on the potential law of logarithmic regression that is derived from statistical analysis between instantaneous rain estimation obtained with a radar in surface and cloud top temperature (T) derived from infrared band of the satellite. The estimation of the rate of rain (R, regression curve) (equation 1) is shown in Figure 6, is fit by the humidity, growth rate and temperature gradient factors (Vicente et al. 1998) and the parallax and orography factors (Vicente et al. 2002)

(1)

Where:

R = Rainfall rate (mm/h)

T = Cloud top temperature (K)

Figure 6: Rainfall rate and Temperature GOES (Vicente et al., 1998)

## 3 Methodology

The study area is between the lengths 75.00ºW and 75.25 ºW and latitudes 11.88 ºS and 12.12 ºS (Shullcas River Subbasin) is shown in Figures 7 and 8. The period of study includes the summer season of 2001 and 2002

Figure 7: Mantaro basin (IGP 2005)

Figure 8: Shullcas river subbasin

The precipitation estimation techniques were implemented in Fortran 90, while the maps were made using Grid Analysis and Display System (GrADS). A 4X4 Km mask was generated for the Shullcas River Subbasin.

As an example, the precipitation estimates for January 22 2001, are shown for both techniques (Figures 9 and 10)

Figure 9: CST/TMI

Figure 10: Hydro-estimator

4 Preliminary Results

The spatially averaged daily precipitation for the summer seasons of 2001 and 2002 has been calculated, for the subbasin. The correlation between both techniques is 0.4 (Figure 11).

The correlation with station rainfall

data is lower still (<0.3), which might be partly a result of the lack of representability of point-measurements of rainfall associated with the strong spatial variability of rainfall. This will be addressed by using observed river discharge data of rainfall, as this is a spatially-integrated measure of rainfall.

However, there are also indications that perhaps the assumed relationship between cloud-top temperature and rainfall underlying the estimation techniques might not be adequate for this region. This possibility is currently under investigation.

Figure 11: Scatterplot between rainfall estimated from CST/TMI and Hydro-estimator, summer 2001 y 2002.

5 References

- Adler, R. F; Negri, A. J., 1988: A satellite infrared technique to estimate tropical convective and stratiform rainfall. Journal Applied Meteorology, 27, 30-51.

- Fashé, R., 2005: Estimación de la Cantidad de Lluvia sobre Perú con Imágenes del Satélite GOES-8. Tesis de Maestría en Física, Facultad de Ciencias Físicas, UNMSM, p 1-96.

- Instituto Geofísico del Perú, 2005.a: Atlas Climático de Precipitación y Temperatura del aire en la cuenca del río Mantaro. Fondo Editorial del Consejo Nacional del Ambiente. Lima-Peru.

- Negri, A. J.; Xu, L.; Adler, R. F., 2002: A TRMM-Calibrated infrared rainfall algorithm applied over Brazil. Journal of Geophysical Research, 107 [D20], 8048-80-62.

- Segura C. B.; Mosquera V. K.; Silva V. Y. Monthly and annual average of the precipitation for the Mantaro river basin from images of GOES satellite. In: International Conference on Southern Hemisphere Meteorology and Oceanography (ICSHMO), 8., 2006, Foz do Iguaçu. Proceedings.. São José dos Campos: INPE, 2006, p. 1175-1180. CD-ROM. ISBN 85-17-00023-4.

- Vicente, G. A., R. A. Scofield, and W. P. Menzel, 1998:The Operational GOES Infrared Rainfall Estimation Technique, Bulletin of American Meteorological Society 79, 1883-1898.

- Vicente, G. A., J. C. Davenport, and R. A. Scofield, 2002: The role of orographic and parallax corrections on real time high resolution satellite rainfall estimation, Int. J. Remote Sens., 23, 221-230.

# Footnotes

Correspondence to: B. Segura (bsc_berlin@hotmail.com)

Geostationary Operational Environmental Satellite

Tropical Rainfall Measuring Mission

Convective-Stratiform Technique/TRMM Microwave Radiometer